26.6.1 I2 Control register 1 (I2C_CR1)
Reset value: 0x0000

15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
SWRST	RFU	ALERT	PEC	POS	ACK	STOP	START	NO / STRETCH	ENGC	ENPEC	ENARP	SMB TYPE	RFU	SMBUS	PE
Rw		Rw	Rw	Rw	Rw	Rw	Rw	Rw	Rw	Rw	Rw	Rw		Rw	Rw

26.6.2 I2 Control register 2 (I2C_CR2)
Reset value: 0x0000
15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RFU			LAST	DMAEN	ITBUFEN	ITEVTEN	ITERREN	RFU		FREQ[5:0]
			Rw	Rw	Rw	Rw	Rw			Rw	Rw	Rw	Rw	Rw	Rw

26.6.6 I2C Status register 1(I2C_SR1)
Reset value: 0x0000
15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
SMB / ALERT	TIME / OUT	RFU	PEC / ERR	OVR	AF	ARLO	BERR	TxE	RxNE	RFU	STOPF	ADD / 10	BTF	ADDR	SB
rc_w0	rc_w0		rc_w0	rc_w0	rc_w0	rc_w0	rc_w0	R	R		R	R	R	R	R

26.6.7 I2C Status register 2(I2C_SR2)
Reset value: 0x0000
15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
PEC[7:0]								DUALF	SMB HOST	SMB / DFLT	GEN CALL	RFU	TRA	BUSY	MSL
R	R	R	R	R	R	R	R	R	R	R	R		R	R	R

Note: Reading I2C_SR2 after reading I2C_SR1 clears the I2C_SR1_ADDR flag, even if the I2C_SR1_ADDR flag was set after reading I2C_SR1. Consequently,
I2C_SR2 must be read only when I2C_SR1_ADDR is found set in I2C_SR1 or when the I2C_SR1_STOPF bit is cleared.

26.6.8 I2C Clock control register (I2C_CCR)
Reset value: 0x0000

15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
F/S	DUTY	RFU		CCR[11:0]
Rw	Rw			Rw	Rw	Rw	Rw	Rw	Rw	Rw	Rw	Rw	Rw	Rw	Rw

Bit 15 F/S: I2C master mode selection
	0: Sm mode I2C
	1: Fm mode I2C

Bit 14 DUTY: Fm mode duty cycle
	0: Tlow / Thigh = 2
	1: Tlow / Thigh = 16/9 (see CCR bits)

Bits 11:0 CCR[11:0]: Clock control register in Fm/Sm mode (Master mode). / Controls the SCL clock in master mode.
	Sm mode or SMBus: / Thigh = CCR * TPCLK1 / Tlow = CCR * TPCLK1
	Fm mode: / if DUTY=0: / TODO: / if DUTY=1: / TODO:

26.6.9 I2C TRISE register (I2C_TRISE)
Reset value: 0x0002
15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
RFU										TRISE[5:0]
										Rw	Rw	Rw	Rw	Rw	Rw

Bit 5:0 TRISE[5:0]: Maximum rise time in Fm/Sm mode (Master mode)

9.1.11 GPIO configurations for device peripherals
table 27. I2C
I2C pinout	Configuration	GPIO configuration
I2Cx_SCL	I2C clock	Alternate function open drain
I2Cx_SDA	I2C Data IO	Alternate function open drain

9.3.9 I2C1 alternate function remapping
table 55. I2C1 remapping
Alternate function	I2C1_REMAP=0	I2C1_REMAP=1
I2C1_SCL	PB6	PB8
I2C1_SDA	PB7	PB9